## Slide 1
Knowledge-Based System
Soil data
(e.g., soil water content, particle size distribution, density)
Geophysical properties relevant to GPR
Expert knowledge
(e.g., information on site, environment, GPR system)
GPR suitability
Geophysical data
(e.g., antenna frequency, permittivity, electrical conductivity, attenuation)
Enhanced GPR data interpretation

## Slide 2: KBS suitability
Suitability Index (SI) definition:
insufficient data 0
very high suitability 1
high suitability 2
moderate suitability 3
low suitability 4
very low suitability 5

## Slide 3: KBS sections
Geophysical data
Soil data
Expert knowledge
Output

## Slide 4: Section 1. Geophysical data
#1 - Are any of the following known (e.g. from previous surveys)?
parameter | unit | symbol
mean depth of available data | m | depth
frequency | MHz | f
apparent permittivity | - | Ea
real permittivity | - | Er
imaginary permittivity | - | Ei
real permittivity at 100 MHz | - | Er.100
imaginary permittivity at 100 MHz | - | Ei.100
real permittivity at 1000 MHz | - | Er.1000
imaginary permittivity at 1000 MHz | - | Ei.1000
apparent permittivity at 100 MHz | - | Ea.100
apparent permittivity at 1000 MHz | - | Ea.1000
magnitude of dispersion | - | Mdisp
bulk electrical conductivity | mS/m | BEC
magnetic permeability | - | mu
attenuation coefficient | dB/m | alpha
skin depth | m | skin.depth
attenuation loss at depth: 1 m, freq: 100 MHz | dB | La.1m.100
attenuation loss at depth: 1 m, freq: 1000 MHz | dB | La.1m.1000
attenuation loss at depth: 1 m, freq: f | dB | La.1m
attenuation loss at depth: depth, freq: f | dB | La
propagation velocity | m/s | v

## Slide 5: Section 1. Geophysical data
The KBS will try to calculate Mdisp, BEC and La and will output all available and calculated geophysical parameters. If no geophysical information is available, the KBS will try to calculate geophysical data from geotechnical data (see section 2).
Key parameters:
Magnitude of dispersion (Mdisp.geophysical)
Bulk Electrical Conductivity (BEC)
Attenuation Loss (La)

## Slide 6: Section 1. Geophysical data
Magnitude of dispersion (from geophysical data) criteria:
# Mdisp classes (Thomas et al., 2010a):
# Mdisp.geophysical.class1: Mdisp < 6 SI = 1
# Mdisp.geophysical.class2: 6 < Mdisp <= 12 SI = 2
# Mdisp.geophysical.class3: 12 < Mdisp <= 18 SI = 3
# Mdisp.geophysical.class4: 18 < Mdisp <= 24 SI = 4
# Mdisp.geophysical.class5: Mdisp > 24 SI = 5

## Slide 7: Section 1. Geophysical data
Bulk Electrical Conductivity criteria:
# BEC classes (Davis and Annan, 1989 and Doolittle et al., 2010):
# BEC.class1: BEC <= 50 mS/m SI = 1
# BEC.class2: 50 < BEC <= 100 mS/m SI = 2
# BEC.class3: 100 < BEC <= 150 mS/m SI = 3
# BEC.class4: 150 < BEC <= 200 mS/m SI = 4
# BEC.class5: BEC > 200 mS/m SI = 5

## Slide 8: Section 1. Geophysical data
Attenuation loss (dB) criteria:
# these classes are identified based on the attenuation loss at the input frequency and depth: 1 m (no matter the input depth)
# if input frequency is not available, attenuation loss for a 250 MH antennas is used
# La.class1: La <= 40 SI = 1
# La.class2: 40 < La <= 60 SI = 2
# La.class3: 60 < La <= 80 SI = 3
# La.class4: 80 < La <= 100 SI = 4
# La.class5: La > 100 SI = 5

## Slide 9: Section 2. Soil data
#2 - Are any of the following known (e.g. from BGS databases, Digimap)?
parameter | unit | symbol
percentage of sand (2mm - 0.05mm) | %w | sand
percentage of clay (< 0.002mm) | %w | clay
percentage of gravel (> 2mm) | %w | gravel
percentage of volumetric water content | %v | vwc
percentage of gravimetric water content | %v | gwc
bulk density | g/cm3 | bulkD
dry density | g/cm3 | dryD
particle density | g/cm3 | partD
density factor (0.9 - 1.3) | - | DF
liquid limit | %w | LL
plastic limit | %w | PL
plasticity index | %w | Ip
linear shrinkage | %w | Ls
soil temperature | °C | temp
organic matter | % | OM
sodium absorption ratio | - | SAR
calcium carbonate content | % | CaCO3

## Slide 10: Section 2. Soil data
The KBS will apply dielectric mixing models (e.g. Peplinski et al., 1995a and b; Mironov et al., 2009) to estimate soil EM properties from geotechnical data. The KBS will also provide a Mdisp class based on more qualitative relationships (e.g. high liquid limit generally corresponds to high dispersion).
Key parameters:
Magnitude of dispersion (Mdisp.geotechnical)
Clay content (clay)
Sodium Absorption Ratio (SAR)
Calcium carbonate content (CaCO3)
Note: an extra parameter currently not included could be the depth of the water table, but it needs further information to justify the assignment to SI classes.

## Slide 11: Section 2. Soil data
Magnitude of dispersion (from geotechnical data) criteria:
# liquid limit classes (based on typical liquid limit values for different soils):
# LL.class1: LL <= 30 % SI = 1
# LL.class2: 30 < LL <= 60 % SI = 3
# LL.class3: LL > 60 % SI = 5
# linear shrinkage classes (Fig.9 in Thomas et al., 2010a):
# LL.class1: Ls <= 8 % SI = 1
# LL.class2: 8 < Ls <= 15 % SI = 3
# LL.class3: Ls > 15 % Si = 5
# plasticity index classes (Table 2 in Thomas et al., 2010a):
# Ip.class1: Ip <= 20 % SI = 1
# Ip.class2: 20 < Ip <= 40 % SI = 3
# Ip.class3: Ip > 40 % SI = 5

## Slide 12: Section 2. Soil data
Clay content criteria:
# clay classes (%w), Doolittle et al., 2007:
# clay.class1: clay <= 10 %w SI = 1
# clay.class2: 10 < clay <= 18 %w SI = 2
# clay.class3: 18 < clay <= 35 %w SI = 3
# clay.class4: 35 < clay <= 60 %w SI = 4
# clay.class5: clay > 60 %w SI = 5

## Slide 13: Section 2. Soil data
Sodium Absorption Ratio (SAR) criteria:
# SAR classes (Doolittle et al., 2007):
# SAR.class1: SAR < 13 # very high suitability SI = 1
# SAR.class2: SAR >= 13 # very low suitability SI = 5
Note: further classes should perhaps be identified but the literature does not provide sufficient information.

## Slide 14: Section 2. Soil data
Calcium Carbonate criteria:
# CaCO3 classes (Doolittle et al., 2007 and 2010):
# CaCO3.class1: CaCO3 < 10 # very high suitability SI = 1
# CaCO3.class1: CaCO3 >= 10 # low suitability SI = 4
Note: further classes should perhaps be identified but the literature does not provide sufficient information.

## Slide 15: Section 2. Soil data
Water table proposed criteria:
# water.table.class1: water.table > 10 m SI = 1
# water.table.class2: 6 < water.table <= 10 m SI = 2
# water.table.class3: 4 < water.table <= 6 m SI = 3
# water.table.class4: 2 < water.table <= 4 m SI = 4
# water.table.class5: water.table <= 2 m SI = 5
Note: any comments on this are welcome

## Slide 16: Section 3. Expert Knowledge (user input)
#3 - Choose one the following information.
    Surface type (if not known try Google Earth, Google Map or other sources):
      Paved surface (e.g., asphalt, cement, paving slabs). SI = 1
      Grass or bare soil (including unpaved roads). SI = 2
      Not known or none of the above. SI = 0
    Surface conditions (valid also for unpaved surfaces. If not known try Google Earth, Google Map or other sources):
      Very good (smooth surface and no cracks)Good (some surface roughness and/or only few cracks, minor water infiltration). SI = 1
      Fair (some rough surface and/or cracks). SI = 3
      Very bad (very rough surface and/or many cracks). SI = 4
      Not known. SI = 0

## Slide 17: Section 3. Expert Knowledge (user input)
    Geomorphology:
      The site is elevated with respect to the surroundings and is unlikely to accumulate an excess of water during rainfall events. SI = 1
      The site is on a depressed area (e.g., valley, dip) and it is likely to accumulate an excess of water during rainfall events. SI = 2
      Not known. Si = 0
    Metallic structures (above and below the ground, excluding the targets):
      Negligible presence of interfering metal structures. SI = 1
      Abundance of metal structures above the ground. SI = 3
      Abundance of buried metal objects (e.g., rebar). SI = 5
      Not known. SI = 0

## Slide 18: Section 3. Expert Knowledge (user input)
    Target type:
      Metallic and with diameter greater or equal to 200 mm. SI = 1
      Metallic and with diameter smaller than 200 mm OR non metallic with diameter greater or equal to 200 mm. SI = 2
      Non metallic and with diameter smaller than 200 mm. SI = 3
      Not known. SI = 0
    Ground clutter (presence of objects of the dimension > 60 mm (e.g. cobbles, boulders) in the soil that cause unwanted reflections):
      Absence or negligible ground clutter caused by coarse particles and buried objects. SI = 1
      Abundance of ground clutter producing significant unwanted multiple reflections. SI = 3
      Not known. SI = 0
    Clay type (from user input):
      Clays with low activity and/or low shrink-swell capacity. SI = 1
      Clays with high clay activity and/or high shrink-swell capacity. SI = 3
      Not known. SI = 0

## Slide 19: Section 3. Expert Knowledge (user input)
    Recent weather:
      No or negligible precipitation events in the past 3 days. SI = 1
      Occurrence of heavy or persistent precipitation events in the past 3 days. SI = 3
      Not known. SI = 0
      If recent.weather == "b" && geomorphology == "b“ SI = 4
    Saturation:
      The soil is thought to be very dry (after a prolonged periods of dry conditions). SI = 1
      The soil is thought to be very wet or saturated (after prolonged periods of wet conditions). SI = 3
      Not known. SI = 0
      If saturation == "b" && geomorphology == "b“ SI = 4

## Slide 20: Section 3. Expert Knowledge (user input)
    GPR system characteristics
      GPR is mechanically suited to grass and unpaved surfaces AND is coupled to the ground surface. SI = 1
      GPR is coupled to the ground surface but is not mechanically suited to grass and unpaved surfaces.
      If GPR.system == "b" && surface.type == "a“ SI = 1
      If GPR.system == “a" && surface.type == “b“ SI = 3
      GPR is not coupled to the ground surface (i.e., antenna is suspended above the ground). SI = 3
      Not known. SI = 0
    GPR suitability from previous experience (i.e. user experience/knowledge, previous use of KBS):
      Very high. SI = 1
      High. SI = 2
      Moderate. SI = 3
      Low. SI = 4
      Very low. SI = 5

## Slide 21: Section 4. Output
The KBS combines the previous information and provides the suitability (from 0 to 5) based on the highest (i.e. most limiting) score for the following sections, so that the user is informed on where the main issues are:
Soil suitability
Site suitability
Environment suitability
System suitability
A warning is issued if the data are insufficient or sparse.
The KBS also provides a ‘final’ suitability based on the highest score of the above sections.
As part of the output the KBS prints all the inputs and the parameters that it was possible to calculate (e.g. signal propagation velocity).